KeyCap 2.0.0.X
by Tim Stair

# Introduction
KeyCap is a windows application for remapping keyboard input to keyboard and/or mouse output (remapped “input” to the operating system).
# Warning
KeyCap should be used AT YOUR OWN RISK. The author of the application is not responsible for any damages caused by its use (however unlikely).
# User Interface
## Main Window
File Menu Item	Function
New	Resets the application to an empty set of key mappings and no configuration file
Open...	Opens a KeyCap configuration file
Save	Saves the current set of key mappings to a configuration file
Save As...	Saves the current set of key mappings to a new configuration file
Exit	Exits the application

Recent Configurations Menu Item	Function
(variable)	Selecting an entry will attempt to load the specified KeyCap configuration file

## Context Menu
The menu is visible by right clicking on the icon in the taskbar.
File Menu Item	Function
Toggle	Toggles key capture on/off
Restore Configuration	Restores the Configuration Window
Exit	Exits the application

## Exiting
The application only exits when the menu items are used. The Close (X) button in the upper right will only hide the window.
# Adding Key Mappings
## Setup an Input Key
1. Click in the Input Key textbox (it will turn yellow indicating it is focused).
2. Press the key on the keyboard to use as the input. Do not press any of the desired modifier keys (Control/Shift/Alt).
3. Specify any modifier keys by checking the appropriate boxes for the input.
## Setup an Output Key
1. Click in the Output Key textbox (it will turn yellow indicating it is focused)
2. Press the key on the keyboard to use as the output. Do not press any of the desired modifier keys (Control/Shift/Alt).
3. Specify any modifier keys by checking the appropriate boxes for the output. There are also special output options described further in the document.
## Add the Key Mapping to the configuration
Click the Add button to add the key mapping
# Enabling Key Capture
Pressing the Start button will enable all loaded key mappings. If you have not saved the configuration you will be prompted to do so.
## Toggling Key Capture
You can start and stop key capturing by right-clicking the status icon and selecting toggle.
## Closing the Configuration Window
If you start capturing and close the window and it will only be accessible via the status icon.
# Up / Down Keyboard Events
Windows keyboard events consist of two types of events: key down and key up. Key down is the act of pressing and holding a key while key up is the act of releasing a previously held key. A complete key press consists of both events. Producing multiple of a given event (down for example) is not likely to be interpreted correctly by any application and should be avoided.
When creating an output you can specify to send the keyboard up, down, or both events. If sending both events this is equivalent to a complete key press. With some applications / games you may want to hold a key down until some later time (see Toggle functionality).
# Input Flags / Special Input Functionality
## Long Press
(Work in Progress) Holding down a key for 1 second can be used as a trigger for the given output. If the key is not held for long enough it will be passed through as normal when the key is released (and only when released). The 1 second value may be customizable in the future.
Due to the complexity of the flags, long press can only be used with input keys without modifiers (no shift, alt, or ctrl).
# Output Flags / Special Output Functionality
By default the output flags are set to result in a complete key press (both up & down are checked). Customize your output and create more complex combinations using the various output flags.
Output	Description
Alt / Control / Shift	Includes the specified key as part of the output (up/down flag will apply to this as well).
Mouse	Creates the specified mouse button action (up/down flag will apply to this as well).
Up	Creates an output that indicates the key/button has been released (user has stopped pressing).
Down	Creates an output that indicates the key/button has been pressed (user started pressing). Until an up message is sent the system will act as though the key is being pressed.
Toggle	Described below this table.
Nothing	If this is specified no action will be taken. They keyboard input will be ignored.
Cancel Outputs	This action will cancel any ongoing outputs (any repeating or those with delays). If this is combined with any other outputs only those before the cancel action will be applied.
Repeat	Described below this table.
Delay	Creates a delay before performing the next action specified in the key mapping. This delay is measured in milliseconds (cannot be less than 100).

## Toggle
Toggle causes the input to not trigger the “key up” event until the key is pressed a second time. This allows the user to create keys that map to holding a mouse or keyboard button until pressing the input key again.
At this time toggle may not operate correctly for combinations of multiple non-modifier keys (like A+D or 1+2).
If the output key involves a modifier (alt/ctrl/shift), Toggle will NOT function as expected. This is blocked in the UI. Toggle cannot function in this case as the required input key cannot be correctly pressed. Example: If pressing ‘a’ produces “shift+b” toggled down, ‘a’ would not toggle the output up because ‘shift’ is currently being held down (as interpreted by Windows).
Toggle Work Around for Shift/Alt/Ctrl Outputs
To work around this do not use a toggle but define another entry that uses the modifier on the same input key.
Example: Define 2 keys:
Input: F10 Output: Shift+W (down event)
Input: Shift+F10 Output: Shift+W (up event)
The important part of this is that you can still just use F10 as your toggle because the operating system will still think the Shift key is being held down from the initial output.
## Repeat
Repeat will attempt to repeat the Output key until the input key is pressed again. This can only be used with complete up+down outputs. By default a minimum delay of 100ms is applied. This can be customized by setting the numeric field of the output (100ms or more). Do not check “delay” in this case as it will override your desired output.
If multiple outputs are specified
- only those flagged as repeat will be repeated
- the highest repeat time will be used (minimum 100ms)
## Appending Key Mappings
This functionality allows you to map additional outputs to an input key. Each appended key will trigger as indicated by the order. At this time there is no way to re-order the output once you have defined it.
This functionality is not extensively tested and may result is unpredictable results. Proceed with caution.
## Add Output String
This functionality attempts to create an output consisting of the keys specified by the user. Upper and lowercase characters are supported. All other settings related to the output configuration are ignored.
NOTE: Due to keyboard mapping issues (hopefully resolvable) only the basic US 104-key keyboard layout is generally supported for special characters.
# Long Running Outputs
A long running output (one involving a delay or repeat) can only have one execution active at a time. Once the output has begun processing the same input will not trigger another. The input keys will still be treated as processed in terms of not passing them to the OS for processing. Upon completion of the output processing the input will once again be able to trigger the output.
# Command Line
Argument	Description
-f <filename>	Will attempt to load the specified file on launch of the application.
-autostart	Will attempt to start the key capture of the loaded file (should be combined with loading a file with -f).